## Slide 1: Fire Safety and Fire Extinguisher Use
Prepared by:
DEXTER T. MANIGBAS, RN
Accredited OSH Practitioner
Pollution Control Officer
Accredited Fire Safety Practitioner
Certified OSH Trainer

## Slide 2: Coverage of this Module:
Workplace Fire Statistics
Workplace Fire Prevention
How Does A Fire Work?
Classes of Fire Extinguishers
Types of Fire Extinguishers
How To Use a Fire Extinguisher
General Fire Safety Tips
Hazard Recognition

## Slide 3: Work Place Fire Statistics
Fires and explosions kill more than 200 and injure more than 5,000 workers each year
BFP requires employers to provide proper exits, fire fighting equipment, and employee training to prevent fire deaths and injuries in the workplace

## Slide 4: More Statistics
There are approximately 6,000 office fires in the United States every year
Major causes of office fires:
  Arson
  Smoking
  Wiring and Appliances

## Slide 5: Fire Prevention
Arson
  Pay close attention to security measures
  Lock doors and windows after business hours
  Keep areas around the building well-lit and clear of combustibles
  Pay attention to housekeeping within the building as well

## Slide 6: Fire Prevention
Smoking Materials
  Use large, non-tip ashtrays in areas where smoking is allowed
  Make sure ashtray contents are cold before emptying
  Make sure no one leaves smoldering cigarettes in wastebaskets
  Prohibit smoking in hazardous areas
  Strictly implement policies with regards to smoking premises and non smoking in the project.

## Slide 7: Fire Prevention
Wiring & Appliances
  Designate an employee to turn off and unplug all appliances at the end of the day (including coffee makers)
  Do not overload outlets
  Replace broken or cracked electrical cords

## Slide 8: Hazards to Avoid
Missing or broken fire safety equipment
Burned out exit lights
Accumulated trash
Propped open fire doors
Blocked stairways
No proper trainings and information in fire preventive measures

## Slide 9: How Does a Fire Work?
All three fire triangle components are needed for a fire to start/continue burning
Fire extinguishers remove one or more of these components

## Slide 10
CLASSES OF FIRE
Class A - Wood, paper, cloth, trash, etc… (A - Ash)
Class B - Flammable liquids, oil, gas, grease, etc... (B - Barrel)
Class C - Energized electrical equipment (C - Circuit)

## Slide 11: CLASSES OF FIRE
Class D – metal type of fire (Type D Fire)
Class K – Kitchen type Fire (commercial cooking oil)

## Slide 12: Types of Fire Extinguishers
The 4 most common are:
  All-Purpose Water
  Carbon Dioxide
  Multi-Purpose Dry Chemical
  Dry Powder
Each has a specific use

## Slide 13: All Purpose Water Type
Use on Class A fires (cooling effect)
Pressurized water
Pressure gauge present

## Slide 14: Carbon Dioxide
Use on Class B and Class C fires
Hard, plastic nozzle
No pressure gauge

## Slide 15: Multi – Purpose Dry Chemical Type
Use on Class A, Class B, and Class C fires
Fine powder under pressure
Pressure gauge present

## Slide 16: How to Use a Fire Extinguisher

## Slide 17: P.A.S.S. Method
Pull the pin

## Slide 18: P.A.S.S. Method
Aim at the base of the fire

## Slide 19: P.A.S.S. Method
Squeeze the handle

## Slide 20: P.A.S.S. Method
Sweep side to side

## Slide 21: When Dealing with Fire
NEVER fight a fire if:
You do not have the proper extinguisher or equipment
The fire has spread beyond its point of origin
Your instincts tell you to “GET OUT!!”

## Slide 22: Proper Care for Fire Extinguisher
Random Testing for supplied Fire Extinguisher
Inspect:
  Monthly (Employee)
  Annually (Competent Professional)
Mount in designated/conspicuous locations
Mount near exits
Recharged or Replaced out of charge / pressure fire extinguishers

## Slide 23: Conduct Training
Types of fire extinguishers
How to use an extinguisher (fire fighting demonstration)
Location of fire extinguishers
Extinguisher limitations
HANDS ON TRAINING IS REQUIRED!

## Slide 24: ENERGENCY EVACUATION / EMERGENCY PREPAREDNESS PLAN
Provision of Emergency Evacuation Plan per Level or Area of Construction Wordplace.
Conduct Training on Emergency Preparedness (Emergency Drills, Emergecy Evacuation, Emergency Preparedness and Response)
Provide Information, Awareness and Education proper to all workers regarding Fire Prevention.
Information regarding Fire Exit of the areas and Fire Fighting Equipment Location (Fire Extinguishers)

## Slide 25
THANK YOU SO MUCH!!!!!
-END OF SLIDE-