## Slide 1: COSH CONSTRUCTION OCCUPATIONAL SAFETY & HEALTH COURSE
MATERIALS HANDLING AND STORAGE

## Slide 2: MATERIALS HANDLING
A technique which includes the art of lifting, placing, storing or moving of materials through the use of appropriate handling equipment and men.

## Slide 3: MATERIALS HANDLING
National Safety Council (NSC) shows that improper materials handling accounts for 20% - 25% of all occupational injuries.
Types of Material Handling Accidents
Physical strain/over-exertion
• Falling load
• Collision
• Hits, cuts, blows
• Trapped between objects
People Falling

## Slide 4: CLASSIFICATION OF MATERIALS HANDLING OPERATION
Manual Handling
is the of lifting, transporting and packaging of products using own physical strength.
Hand operated handling, transporting and packaging of products.
Mechanical Handling
pertains to more rigid, powered and non-powered mechanics mainly for handling bulky and heavy items

## Slide 5: MANUAL HANDLING – MISTAKES THAT CAUSE INJURIES
Bending Back
Twisting with load
Attempting to much weight (load too heavy)
Reaching too far
Lifting to one side
Off-balance shifting
Failure to use personal PPE, such as gloves

## Slide 6: PRECAUTIONS IN MANUAL HANDLING
Familiarize with the hazard associated with the material or load
  Sharp edges?
  Too heavy?
  Contains hazardous material? (check MSDS)
• Examine the surrounding area prior to handling
• Get a firm grip of the object
• Use necessary personal protective equipment
• Lift gradually
• Follow proper lifting method.

## Slide 7: HUMAN BODY ANATOMY
WEAK
STRONG
Your Back
Your Legs
Protect it
Use their power to lift correctly…. And safely
Meet you body

## Slide 8: LIFTING COMPARISON
Wrong Way
Right Way
Notes: Proper Lifting Technique
– Position the load close to the body
– Maintain a firm grip on the load
– Keep feet apart and bend knees
– Look forward to keep back straight
– Use muscle power of the legs
– Use smooth, controlled movements
– Turn feet in the direction of the movement and do not twist
• Proper Carrying Technique
– Hold the load close so you can see over it
– Keep the load balanced
– Use smooth, controlled movements
– Turn feet in the direction of the
movement and do not twist
– Watch out for pinch points –doorways, etc.
- Make sure you’re seeing your path.

## Slide 9: MECHANICAL HANDLING
Non-Power Driven
Wheeler/hand truck
Wheelbarrow
• cart
• drum tilter
• trolley
hand pallet (pallet jack)
• pulley

## Slide 10: MECHANICAL HANDLING
Power Driven
Forklifts
Cranes
Tow Trucks
Conveyors
Power driven hoists
Motorized pallet jacks
Elevators and dumbwaiters

## Slide 11: MECHANICAL HANDLING
Mechanical handling equipment could be categorized into two:
lifting equipment – such as hoists and cranes, drum tilter/lifter
transport equipment – tow trucks, forklifts, conveyors, Wheeler/hand truck, pulley, trolley, carts, pallet jacks (motorized or non-motorized)

## Slide 12: LIFTING EQUIPMENT TYPES
Hoist
  Lever
  Chain
  Electric
Cranes
  Stationary
    Tower cranes,
    Overhead traveling cranes
  Mobile
    Wheel Type
    Crawler Type
    Gantry cranes.

## Slide 13: TRANSPORT EQUIPMENT TYPES
• Forklift
• Tractor-trailer
• Dump Truck
• Conveyor
Tow trucks
Wheeler/hand truck, pulley, trolley, carts
pallet jacks (motorized or non-motorized)

## Slide 14: MECHANICAL HANDLING SAFE PRACTICES
Mechanical equipment offers more power. However, more power oftentimes means more hazards and more severe injuries. The following pre-cautions should be observed when working with some of these mechanical handling equipment:
CONVEYORS - To prevent the possibility of an injury, an emergency button or pull cord designed to stop the conveyor must be installed at the employee's work station. Continuously accessible conveyor belts should have an emergency stop cable that extends the entire length of the conveyor belt so that the cable can be accessed from any location along the belt.

## Slide 15: MECHANICAL HANDLING SAFE PRACTICES
CRANES - Only thoroughly trained and competent persons are permitted to operate cranes. Operators should know what they are lifting and what it weighs.
SLINGS - When working with slings, employers must ensure that they are visually inspected before use and during operation. Riggers or other knowledgeable employees should conduct or assist in the inspection because they are aware of how the sling is used and what makes a sling unserviceable. A damaged or defective sling must be removed from service.
FORKLIFTS - Affected workers should be aware of the safety requirements pertaining to forklift operation.
Notes: The NIOSH report shows that approximately every 3 days, someone in the US is killed in a forklift related accident. Each year, an additional 94,750 injuries related to forklift accidents are reported. The costs incurred due to forklift accidents are estimated to be over a hundred million dollars

## Slide 16: MECHANICAL HANDLING GENERAL REQUIREMENTS
• Operators must be authorized.
• Operators must undergo skills training.
Handlers and operators must be trained in safety and health.
• Equipment must be regularly inspected and maintained.

## Slide 17: THANK YOU!!!!!