## Slide 1: MACHINE SAFETY
Prepared by:
DEXTER T. MANIGBAS, RN
Accredited OSH Practitioner
Pollution Control Officer
Accredited Fire Safety Practitioner
Certified OSH Trainer

## Slide 2: Problem Arise
Workers who operate and maintain machinery each year suffer approximately
  18,000 amputations, lacerations, crushing injuries, and abrasions
  800 deaths

## Slide 3: Common Machineries used in Construction settings:
1.) Bar Cutter
2.) Bar Bender
3.) Grinding Machine
4.) Speed Cutter
5.) Welding Machine
6.) Genset

## Slide 4: Common Incidents Involving use of Machines
Reaching in to “clear” equipment
Not using Lockout/Tag-out
Unauthorized person doing maintenance or using the machines
Missing or loose machine guards
Not returning to properly to its storage
Lack of training
Lack of Instruction proper
Lack of information

## Slide 5: Prevention:
Any machine part, function, or process which may cause injury must be safeguarded.
Where the operation of a machine can injure the operator or other workers, the hazard must be controlled or eliminated
Proper maintenance of the machines.
Authorized and skilled personnel conducting maintenance work.
Proper inspection of the machine prior to use or activity.
Information dissemination (training, instruction and supervision)

## Slide 6: Machine Guarding
Areas of machine needed to be guarded are the following:
1.) Point of Operation
2.) Power Transmission Apparatus
3.) Other Moving / Rotating Parts

## Slide 7: Types of Machine Guarding
Fixed
  Provide secure barrier
Interlocked
  Cuts off power when guard opened or removed
Adjustable
  Barrier manually moved to accommodate stock or operation
Self-adjusting
  Barrier automatically moves to accommodate operation

## Slide 8: Fixed Guarding
Advantages:
  Maximum protection
  Variety of applications
  In-house fabrication
  Low cost & maintenance
Disadvantages:
  Poor visibility
  Must remove for repairs requiring LOTO

## Slide 9: Interlocked Guards
Type of guarding that when removed or opened, stops power.
Advantage
  Maximum protection
  Portion of guard easily removed for access
Disadvantage
  Can be overridden by employee
  High cost
  Maintenance required

## Slide 10: Adjustable Guards
Advantage
  Flexibility
  In-house fabrication
Disadvantage
  Not maximum protection
  Rely on worker to properly position
  May prohibit easy access

## Slide 11: Self Adjusting Guards
Advantage
  Employee not involved in positioning
  Readily available
Disadvantage
  Not maximum protection
  May need frequent fine tuning

## Slide 12: Requirements for Safe Guarding
Prevent contact
Secure, tamper-resistant, and durable
Protect from falling objects
Create no new hazards (residual)
Create no interference
Allow safe lubrication and maintenance
Convenient to the user / workers
Fixed guards should used whenever possible
Machines designed for fixed location shall be secured to prevent movement

## Slide 13: Machine Safety Responsibilities
Management
  ensure all machinery is properly guarded
Supervisors
  train employees on specific guard rules in their areas
  ensure machine guards remain in place and are functional
  immediately correct machine guard deficiencies

## Slide 14: Machine Safety Responsibilities
Employees
  do not remove guards unless machine is locked and tagged
  report machine guard problems to supervisors immediately
  do not operate equipment unless guards are in place

## Slide 15: General Safety Principle
Securely fasten equipment to eliminate movement or “walking”
No loose clothing, long hair, jewelry, or gloves around rotating machine parts
Respect machine guards
Keep electrical cords and plugs intact
Inspect machinery before each use

## Slide 16: General Safety Principle
Do not leave machines running and unattended
Never attend to brush debris from the table surface while the machine is running
An active brake mechanism adds greatly to safety
Easily reached “off” switch increases safety

## Slide 17: Different Types of Machineries in Construction

## Slide 18
THANK YOU SO MUCH!!!!!
-END OF SLIDE-