## Slide 1: COSH CONSTRUCTION OCCUPATIONAL SAFETY & HEALTH COURSE
PERSONAL PROTECTIVE EQUIPMENT (PPE)

## Slide 2: Objectives
distinguish the appropriate type of PPE you need in your workplace
To know the importance of PPE and the proper use
know the limitation of PPE
develop program to introduce PPE for your company

## Slide 3: Rule 1080 Personal Protective Equipment and Devices
1081 GENERAL PROVISIONS:
1081.01 EVERY EMPLOYER:
  Shall at his own expense furnish his workers with protective equipment for the eyes, face, hands and feet, protective shields and barriers whenever necessary by reason of the hazardous nature of the process or environment, chemical or radiological or other mechanical irritants or hazards capable of causing injury or impairment in the function of any part of the body through absorption, inhalation or physical contact.

## Slide 4: Rule 1080 Personal Protective Equipment and Devices
1081.02
All protective equipment shall be of approved design and construction appropriate for the exposure and the work to be performed.
1081.03
The employer shall be responsible for the adequacy and proper maintenance of personal protective equipment used in his workplace.
1081.04
No person shall be subjected or exposed to hazardous environmental condition without protection.

## Slide 5: Defining hazards
A hazard is anything that produces adverse effects on anyone.
  Examples:
    slippery floors
    falling objects
    chemicals

## Slide 6: Classification of hazards
1. Direct
  * Unguarded Machines
  * Falling/Flying Materials
  * Slippery Floors, etc.
2. Physical
  * Noise
  * Temperature Extremes
  *Ionizing/Non-Ionizing Radiation
  * Extreme Pressure
  * Vibration

## Slide 7: Classification of hazards
3. Chemical
  * vapors
  * gas
  * dust
  * fumes
  * mists
4. Biological
  * bacteria
  * virus
  * Fungi
  5. Ergonomic

## Slide 8: Hazard control measures
Engineering
Administrative
PPE

## Slide 9: PROGRAM TO INTRODUCE PPE
1. Written Policy
2. Proper Selection of PPE
3. Proper Training
4. Maintenance Program
5. Incentive System
6. Enforcement

## Slide 10: Proper Training
1. Describing what hazards and/or conditions in the workplace
2. Telling what can be /cannot be done about it
3. Explaining why certain type of PPE has been selected
4. Discussing the capabilities and/or limitation of the PPE

## Slide 11: Proper Training
5. Demonstrating how to use, adjust or fit PPE
6. Practicing using PPE
7. Explaining company how to deal with emergencies
8. Discussing how PPE will be paid for, maintained, repaired and cleaned.

## Slide 12
Should be taken as the last thin line of defense.
Does not reduce the hazard.
Merely set up a frail barrier.
Must be constantly maintained.
FACTORS TO CONSIDER IN
THE USE OF PERSONAL
PROTECTIVE EQUIPMENT

## Slide 13
The NEED for personal protective equipment must be established.
  Present the need for the device, based on exposure and nature of works
The problem of SELECTING the right type. Two criteria should be used:
  The degree of protection which a particular piece affords under varying conditions, and
  The ease with which it may be used.
    Degree of protection must be proportional to seriousness of hazard.
    Balance between protection and interference.
    Quality of PPE & Factor of Cost.
The next problem is that of having workers WEAR personal protective equipment once it has been chosen.
  Acceptability of PPE to worker.
PPE SELECTION AND USE

## Slide 14
Present the need for the device.
Inform worker on area demands and how to use the equipment.
Give worker opportunity to select.
Keep stock of PPE available.
Keep stockroom neat and clean.
Replace worn-out PPE immediately.
Set Example.
Disciplinary sanctions are there to protect the worker.
APPROACHES TO COUNTER
NEGATIVE ATTITUDES

## Slide 15
HEAD AND EAR PROTECTION
  protective or hard hats, caps
  hair protectors
  ear protectors
    Ear plugs
    Ear Muffs
CLASSIFICATION OF PPE

## Slide 16: TYPES OF HARD HAT
Hard hats are divided into three industrial classes:
 Class A hard hats provide impact and penetration resistance along with limited
voltage protection (up to 2,200 volts).
 Class B hard hats provide the highest level of protection against electrical
hazards, with high-voltage shock and burn protection (up to 20,000 volts). They
also provide protection from impact and penetration hazards by flying/falling
objects.
 Class C hard hats provide lightweight comfort and impact protection but offer no
protection from electrical hazards.
Another class of protective headgear on the market is called a “bump hat,” designed for
use in areas with low head clearance. They are recommended for areas where
protection is needed from head bumps and lacerations, but don’t protect against falling
or flying objects and are not ANSI-approved.

## Slide 17: TYPES OF HARD HAT
Each hat should bear a label inside the shell that lists the manufacturer, the ANSI
designation and the class of the hat.

## Slide 18
Noise Reduction
EAR PLUGS: 7 – 10 dBA
EAR MUFFS: 20 – 25 dBA

## Slide 19: HEARING PROTECTION
Some types of hearing protection include:
 Single-use earplugs are made of waxed cotton, foam, silicone rubber or
fiberglass wool. They are self-forming and, when properly inserted, they work as well as most molded earplugs.
 Pre-formed or molded earplugs have to be fitted for you by a professional, and can be disposable or reusable. Reusable plugs should be cleaned after each use.
 Earmuffs require a perfect seal around the ear. Glasses, facial hair, long hair or facial movements such as chewing can reduce the protective value of earmuffs.

## Slide 20: HEARING PROTECTION
Generally, the louder the noise, the shorter time employees can listen to it before they need hearing protection. For instance, 85 dB (as loud as normal traffic) over a full work day is the lowest level at which hearing protection is required.
 A noise level of 95 dB is ten times as loud, and your exposure should be limited to six hours or less.
 A noise at 115 dB (what you would hear at the front row of a rock concert) is only safe to listen to for about 15 minutes.

## Slide 21
FACE AND EYE PROTECTION
  Hoods
  Spectacles and goggles
  Face shields
  Welding mask

## Slide 22: EYE AND FACE PROTECTION
Many eye injuries occur because workers are not wearing any eye protection, while others result from wearing improper or poorly-fitting eye protection.
Always wear whatever eye and face protection is appropriate; always make sure it fits properly.

## Slide 23: EYE AND FACE PROTECTION
Normal prescription corrective lenses are not enough protection for construction situations. If you usually wear corrective lenses, your employer should provide PPE that
fits over your glasses or incorporates your prescription.
Protective eyewear should never interfere with the proper positioning of your prescription, because vision is important on every worksite.

## Slide 24: TYPES OF EYE AND FACE PROTECTION
Some of the most common types of eye and face protection are listed below.
 Safety spectacles have frames constructed of metal or plastic and impact resistant lenses made of impact-resistant material (usually plastic). Side shields are available on some models.
 Goggles are tight-fitting eye protection that completely covers the eyes, the eye sockets, and the facial area immediately surrounding the eyes. They protect against impact, dust, and splashes. Some goggles are designed to fit over prescription corrective lenses.

## Slide 25: TYPES OF EYE AND FACE PROTECTION
Some of the most common types of eye and face protection are listed below.
 Welding shields are constructed of vulcanized fiber or fiberglass and fitted with a filtered lens, and protect eyes from burns caused by infrared or intense radiant light. They also protect both the eyes and face from flying sparks, metal spatter, and slag chips produced during welding, brazing, soldering and cutting operations. The shade number of the lens should be high enough to protect against the specific dangers of your job.

## Slide 26: TYPES OF EYE AND FACE PROTECTION
Some of the most common types of eye and face protection are listed below.
 Face shields are transparent sheets of plastic that extend from the eyebrows to below the chin and across the entire width of the employee’s head. Some are polarized for glare protection. Face shields protect against nuisance dusts and
potential splashes or sprays of hazardous liquids but will not provide adequate protection against impact hazards. Face shields used in combination with goggles or safety spectacles will provide additional protection against impact
hazards.

## Slide 29
RESPIRATORY PROTECTION
  Oxygen or air breathing apparatus (SCBA)
  Supplied air respirators
  Canister and cartridge respirators
  Dispersoid filter respirators

## Slide 32
HAND, FOOT, AND LEG PROTECTION
  Gloves, mitts, hand leathers
  Safety shoes
  Foot guards
  Leggings

## Slide 33: FOOT PROTECTION
Examples of situations in which foot and/or leg protection are required include:
 When heavy objects, like barrels or heavy tools, might roll or fall on someone’s
feet
 When employees working with sharp objects, such as nails or spikes, that could
pierce the bottom or top of a pair of ordinary shoes
 Exposure to molten metal that might splash on feet or legs

## Slide 34: FOOT PROTECTION
Examples of situations in which foot and/or leg protection are required include:
 Working on or around hot, wet, or slippery surfaces
 Working when electrical hazards are present.

## Slide 35: FOOT PROTECTION
Safety shoes have impact-resistant toes and heat-resistant soles that protect the feet against hot work surfaces, like the ones encountered in paving operations.

## Slide 36: FOOT PROTECTION
Safety-toe footwear for employees shall meet the requirements and specifications in ASTM F-2412-2005, Standard Test Methods for Foot Protection, and ASTM F-2413- 2005, Standard Specification for Performance Requirements for Protective Footwear,

## Slide 37: SPECIAL PURPOSE SAFETY SHOES
In the rare case where a construction worker is in a location with an explosive hazard, electrically conductive shoes may be appropriate. They provide protection against the buildup of static electricity.
Electrical hazard, safety-toe shoes are nonconductive, and will prevent the wearers’ feet from completing an electrical circuit to the ground. These shoes can protect against open circuits of up to 600 volts in dry conditions

## Slide 38: HAND PROTECTION
TYPES OF GLOVES:
Leather, Canvas, or Metal Mesh Gloves
Sturdy gloves made from metal mesh, leather or canvas provide protection against cuts
and burns. Leather or canvas gloves also protect against sustained heat.
 Leather gloves protect against sparks, moderate heat, blows, chips and rough
objects.

## Slide 39: HAND PROTECTION
TYPES OF GLOVES:
Leather, Canvas, or Metal Mesh Gloves
 Aluminized gloves provide reflective and insulating protection against heat and
require an insert made of synthetic materials to protect against heat and cold.
 Aramid fiber gloves protect against heat and cold, are cut- and abrasiveresistant and wear well.

## Slide 40: HAND PROTECTION
TYPES OF GLOVES:
Leather, Canvas, or Metal Mesh Gloves
 Synthetic gloves of various materials offer protection against heat and cold, are cut- and abrasive-resistant and may withstand some diluted acids. These materials do not stand up against alkalis and solvents.

## Slide 41: HAND PROTECTION
TYPES OF GLOVES:
Fabric and Coated Fabric Gloves
Fabric and coated fabric gloves are made of cotton or other fabric to provide varying degrees of protection.
 Fabric gloves protect against dirt, slivers, chafing and abrasions. They do not
provide sufficient protection for use with rough, sharp or heavy materials.

## Slide 42: HAND PROTECTION
TYPES OF GLOVES:
Fabric and Coated Fabric Gloves
 Coated fabric gloves are normally made from cotton flannel with napping on one side. By coating the unnapped side with plastic, fabric gloves are transformed into general-purpose hand protection offering slip-resistant qualities.

## Slide 43: HAND PROTECTION
Chemical- and Liquid-Resistant Gloves
Chemical-resistant gloves are made from rubber or plastic.

## Slide 46
F. FALL PROTECTION
SAFETY BELTS & LIFE LINES

## Slide 47
Safety Belts
Safety Harness
D - ring

## Slide 48: BODY PROTECTION
Protective clothing comes in a variety of materials, each effective against particular hazards, such as:
 Paper-like fiber used for disposable suits provide protection against dust and splashes.
 Treated wool and cotton adapts well to changing temperatures, is comfortable, and fire-resistant and protects against dust, abrasions and rough and irritating surfaces.

## Slide 49: BODY PROTECTION
 Duck is a closely woven cotton fabric that protects against cuts and bruises
when handling heavy, sharp or rough materials.
 Leather is often used to protect against dry heat and flames.
 Rubber, rubberized fabrics, neoprene and plastics protect against certain
chemicals and physical hazards. When chemical or physical hazards are
present, check with the clothing manufacturer to ensure that the material
selected will provide protection against the specific hazard.

## Slide 50: Working Over or Near Water
Employees working over or near water, where the danger of drowning exists, shall be provided with approved life jacket or buoyant work vests.

## Slide 51
All PPE must be kept clean and properly maintained.
PPE should be inspected, cleaned at regular intervals.
PPE shall not be shared between employees until it has been properly cleaned and sanitized.
CLEANING & MAINTAINING PPE

## Slide 52
Occupational Safety and Health Center
Safety Control Division
TEST of Personal Protective Equipment
TEST REPORT submitted by supplier of PPE shall be
in original form and in current year.

## Slide 53
OBJECTIVES:
  Verifying issuance of PPE’s.
  Protection of the organization against liability in the event of litigation.
  Controlling cost by identifying over-use and abuse of equipment.
    NOTE: Recommended RETENTION PERIOD for PPE RECORD KEEPING is 1 year to 10 years.
PPE RCORD KEEPING

## Slide 54
Written records shall be kept of the names of persons trained.
Supervisors shall maintain training records for at least 3 yrs.
H&S Committee shall maintain HAC form for each site evaluation for at least 3 yrs.
RECORD KEEPING

## Slide 55
PPE shall be properly stored to protect against environmental conditions that might reduce the effectiveness of the equipment.
PPE, having a shelf-life limitation, shall be checked periodically to ensure compliance with the expiration date.
STORAGE OF PPE

## Slide 56
MANAGEMENT shall:
  Provide PPE and training for personnel.
  Post areas requiring PPE with signs.
  Ensure full compliance of responsibilities of employees set forth in the safety program and/or policies.
SUPERVISORS shall:
  Ensure that appropriate PPE is available to employees.
  Ensure PPE is properly used.
RESPONSIBILITIES

## Slide 57
EMPLOYEES shall:
  Use PPE in accordance with instruction & training received.
  Guard against damage to PPE.
  Care for their PPE properly.
  Report PPE malfunctions or problems to supervisor.
  Follow safe work practices while working with hazardous materials & wastes.
H&S COMMITTEE shall:
  Conducts workplace hazard assessments to determine the need for PPE. Maintains records of hazards assessments.
  Provides training assistance to supervisors on the proper use, care, & cleaning of approved PPE.
  Provides guidance to the supervisor for the selection & purchase of approved PPE.
  Periodically re-evaluates the suitability of previously selected PPE. Reviews, updates, & evaluates the overall effectiveness of the PPE program.