## Slide 1: ELECTRICAL SAFETY
Prepared by:
DEXTER T. MANIGBAS, RN
Accredited OSH Practitioner
Pollution Control Officer
Accredited Fire Safety Practitioner
Certified OSH Trainer

## Slide 2: Electricity Define as:
A physical agency caused by the motion of electrons, protons, and other charged particles, manifesting itself as an attraction, repulsion, magnetic, luminous, and heating effects, etc.

## Slide 3: ELETRICAL MATERIALS
CONDUCTOR – contains many free electrons --- gold, copper, silver, aluminum .
INSULATOR – contains few free electrons-Usually non-metallic such as wood, rubber, glass, etc.

## Slide 4: GENERATING ELECTRICITY
Friction
Pressure
Heat
Light
Chemical Reaction and;
Magnetism

## Slide 5: Objectives:
In this course, we will discuss the following:
Common electrical hazards
Standards relating to those hazards
Electrical equipment defects/hazards
Tools/techniques used in identifying hazards

## Slide 6: Common Common Electrical Hazards
Electric shock/electrocution occurs when current flows through the body damaging the body.
Electrical burns are caused by arc blast or hot conductors.
Indirect falls from ladders, scaffolds, or other walking and working surfaces.

## Slide 7: Common Electrical Hazards
Explosions can be caused when electricity provides a source of ignition for an explosive mixture in the atmosphere.
Fires are caused by overloading a circuit or appliance or by current flowing through high resistance due to faulty wiring, setting fire to insulation and surrounding materials.

## Slide 8: General Requirements:
Electrical equipment must be free from recognized hazards that can cause death or serious physical harm to employees.
  Suitability for installation
  Mechanical strength and
  durability
  Electrical insulation
  Heating effects under
  condition of use
  Arcing effects
  Classification by type, size, voltage,
  current capacity, specific use

## Slide 9: General Requirements
Listed, labeled, or certified equipment must be installed and used in accordance with instructions included in the listing, labeling or certification.

## Slide 11: Splices
  Splicing devices suitable for use
  Welding/brazing/soldering
  Mechanically/electrically secure before soldering
  Covered with insulation equivalent to that of the conductors
  Insulating device suitable for purpose

## Slide 12: General Requirements:
Each service, feeder, and branch circuit, at its disconnecting means or over current device, shall be legibly marked to indicate its purpose.

## Slide 13: General Requirements:
Live parts of electric equipment operating at 50 volts or more shall be guarded against accidental contact by cabinets or other forms of enclosures, or by another suitable method.

## Slide 14: General Requirements:
Employer shall use either ground fault circuit interrupters, or
An assured equipment grounding conductor program to protect employees

## Slide 15: General Requirements:
The path to ground from circuits, equipment, enclosures must be permanent and continuous.

## Slide 16: Wiring Designed and Cable Requirements:
Flexible cords and cables must be protected from damage.

## Slide 17: Wiring Designed and Cable Requirements:
Extension cord sets used with portable electric tools and appliances must be of three-wire type and must be designed for hard or extra-hard usage.

## Slide 18: Wiring Designed and Cable Requirements:
Conductors entering boxes, cabinets, or fittings must be protected from abrasion.

## Slide 19: Wiring Designed and Cable Requirements:
All pull boxes, junction boxes, and fittings must be provided with a cover.
If metal covers are used, they must be grounded.

## Slide 20: Wiring Designed and Cable Requirements:
Flexible cords shall be connected to devices and fittings so that strain relief is provided.
  Will prevent pull from being directly transmitted to joints or terminal screws

## Slide 21: Safety Related Work Practices:
Employer must not permit an employee to work in such proximity to any part of an electric power circuit.
  If employee could contact the power circuit, it must be de-energized or guarded.

## Slide 22: Safety Related Work Practices:
Working spaces, walkways, and similar locations shall be kept clear of cords so as not to create a hazard to employees.

## Slide 23: Safety Related Work Practices:
Worn or frayed electric cords must not be used.
Extension cords shall not be stapled, hung from nails or suspended by wire.

## Slide 24: Lock-out Tag-out
Why use lockout/tagout?
  Protects maintenance personnel from power being reapplied by mistake.
  Recognized hazard
  Employee required to remove or bypass a guard or safety device
  Employee required to place part of body into area that would be a danger zone during machine operation cycle

## Slide 25: Affected Employee:
Job requires employee to
  operate or use a machine or equipment on which servicing or maintenance is being performed under lockout or tag-out, or
  work in an area in which such servicing or maintenance is being performed

## Slide 26: Maintenance Personnel / Authorized Employee
Locks out or tags out machines or equipment in order to perform servicing or maintenance on that machine or equipment
Affected employee whose duties include servicing or maintenance under this section

## Slide 27: Lock - out
Placement of a lockout device on an energy isolating device, in accordance with an established procedure, ensuring that energy isolating device and equipment being controlled cannot be operated until lockout device is removed

## Slide 28: Lock-out Devices:
Device that uses a positive means such as a lock, either key or combination type, to hold an energy isolating device in the safe position and prevent the energizing of a machine or equipment

## Slide 29: Servicing and Maintenance Activities
Workplace activities such as:
  Constructing,
  Installing,
  Setting up,
  Adjusting,
  Inspecting,
  Modifying, and
  Maintaining and/or servicing machines or equipment

## Slide 30: Tag-out
Placement of tag-out device:
  on an energy isolating device,
  in accordance with an established procedure,
  to indicate that energy isolating device and equipment being controlled may not be operated until tag-out device is removed.

## Slide 31: Energy Control Program:
Energy control procedures
Employee training (awareness and instruction and proper supervision)
Periodic inspections
Any employee who services/maintains any equipment where unexpected energizing or stored energy release could cause injury isolates and renders it inoperative first.

## Slide 32: Protective Materials and Hardware:
Lockout devices:
  Substantial enough to prevent removal without excessive force or unusual techniques such as bolt cutters
Tag-out devices:
  Substantial enough to prevent inadvertent or accidental removal
  Non-reusable attachment means
  Attachable by hand, self-lockable
  At least equivalent to nylon cable tie

## Slide 33: Training and Information:
Ensure employees understand purpose and function of energy control program
Ensure employees acquire skills required for safe application, usage, removal of energy controls

## Slide 34: Employee Training and Requirements:
Authorized employee:
  Recognition of hazardous energy sources
  Type and amount of energy in workplace
  Methods and means for energy isolation
Affected employee:
  Purpose and use of procedure
Other employees in area:
  Procedure and prohibition on restarting

## Slide 35: Employee Training forTag-out
Train on limitations of tags:
  Warning devices do not provide physical restraint that a lock would
  Tag not to be removed without owner’s authorization, bypassed, ignored, defeated
  Must be legible / understandable to work
  Must withstand environmental conditions
  False sense of security
  Attach securely: avoid accidental removal

## Slide 36: General Requirements:
Only the authorized / certified well trained employees performing the servicing or maintenance may apply lockout/tag-out.

## Slide 37
THANK YOU SO MUCH!!!!!
-END OF SLIDE-