## Slide 1: DEPARTMENT ORDER No. 13 Series of 1998
Guidelines Governing OSH in the
Construction Industry

## Slide 2: OSH LAWS & ISSUANCES
Book IV, Title I – Medical, Dental and Occupational Safety
Occupational Safety and Health Standards, (OSHS)1978
DO 13 –
Guidelines Governing Safety and Health in the Construction Industry

## Slide 3: Objectives
To ensure the protection and welfare of
workers employed in the construction industry
To ensure protection and welfare of the general public within and around the immediate vicinity of any construction worksite as well as
the promotion of harmonious employer- employee relationships
To take into consideration industry practices and applicable gov’t. requirements

## Slide 4: SALIENT FEATURES OF DEPARTMENT ORDER NO. 13, series of 1998
Department Order No. 13 : Otherwise known as the Guidelines Governing
Occupational Safety and Health in the Construction Industry

## Slide 5: Definitions of Terms
Construction SH Committee - the general SH committee for a construction project site that shall be the overall coordinator in implementing OSH program

## Slide 6: Definitions...
Construction SH Officer - any employee/worker trained and, in addition to the regular duties and responsibilities, tasked by his employer to implement OSH programs in accordance with the provisions of the OSH Standards

## Slide 7: Definitions...
Construction SH Program - a set of detailed rules to cover the processes and practices that shall be utilized in a specific construction site in conformity with the OSHS including the personnel responsible and the penalties for violation thereof.

## Slide 8: Definitions...
Emergency Health Provider - any person or organization who is certified or recognized by DOH and who can provide the same or equivalent emergency health services as an emergency hospital, including emergency treatment of workers on site, emergency transport and care of injured workers to the nearest hospital, with adequate personnel, supplies and facilities for the complete immediate treatment of injuries or illnesses.

## Slide 9: SALIENT FEATURES OF DEPARTMENT ORDER NO. 13, series of 1998
– Section 4: Coverage
The guidelines shall apply to all construction activities, including demolition, whether owned by the private or the government sector

## Slide 10
– Section 5: Construction Safety and Health Program
Before the start of the actual construction, The construction project manager shall prepare and submit to DOLE Regional Office a comprehensive construction safety and health program.
SALIENT FEATURES OF
DEPARTMENT ORDER NO. 13, series of 1998

## Slide 11: Construction Safety and Health Programs
Safety and Health Committee
Safety Policies
Penalties and Sanction
Orientation, Instruction and Training
Waste Disposal

## Slide 12: Construction SH Programs
Executed and verified by the construction project manager or project manager
Shall be submitted to Regional Offices for approval or modification
cost shall be integrated into the project cost, provided it shall be a separate pay item.

## Slide 13: SALIENT FEATURES OF DEPARTMENT ORDER NO. 13, series of 1998
– Section 6: Personal Protective Equipment
All employers must provide personal protective equipment for all employees needing such equipment. All other persons entering the construction site must wear the necessary protective equipment. The equivalent cost for the provision of PPE shall be an integral part of the project cost.

## Slide 14: Personal Protective Equipment
For Specialty Construction Workers
For all other persons authorized or allowed within the construction site
Free of charge

## Slide 15: SALIENT FEATURES OF DEPARTMENT ORDER NO. 13, series of 1998
– Section 7: Safety Personnel
A means of coordination was established wherein the main or general contractor shall have over- all management and coordination of all safety and health officers
/personnel working within the construction site. All full-time safety and health personnel must be accredited by DOLE.

## Slide 16: Safety Personnel
General constructor must provide for a full-time general construction safety and health officer
Additional construction SH Officer depending on the number of workers
Subcontractor’s safety officer

## Slide 17: Safety Personnel Requirement DO 16 & DO 13
Every additional 500 or fraction thereof
1 Additional full-time safety man
1 Safetyman for every 10 units of heavy equipment
Hazardous Workplaces
No. of Workers Safety Personnel
1 – 50 1 Part-time Safety Man
51 – 200 1 Full-time Safety Man
201 – 250 1 Full-time & 1 Part-time Safety Man
251 - 500 2 Full-time Safety Man

## Slide 18: SALIENT FEATURES OF DEPARTMENT ORDER NO. 13, series of 1998
– Section 9: Construction Safety Signages Mandatory provision of safety and
warning signs are reiterated not only for the protection of workers, but also the public in general. Signs should conform with the standard requirements of the OSHS.
 Usage of PPE
 Falling/ falling objects
 Explosives and flammable substances
 Tripping or slipping hazards
 Toxic or irritant airborne contaminants/substances
 Electrical facility
 Dangerous moving parts of machines
 Fire alarms/ fire fighting
 Instructional signs/ Update of man-hours lost
WARNING: Hazardous
Area. All personnel must wear protective
equipment before entry

## Slide 19: SALIENT FEATURES OF DEPARTMENT ORDER NO. 13, series of 1998
– Section 10: Safety on Construction Heavy
Equipment
Pre-Construction
– Operators tested and certified
by TESDA
– Heavy equipment tested and certified by DOLE
or its recognized organizations
During Construction
  Mobilization or transport of heavy equipment
  Standard procedure in erection and dismantling
  Routine inspection

## Slide 20: Construction Safety and Health Committee
Composition Chairperson: Secretary:
Members:
Project Manager
Gen. Construction Safety Officer
Construction Safety Officers Safety Reps. From Sub-con Health Personnel
Worker’s Representatives

## Slide 21: SALIENT FEATURES OF DEPARTMENT ORDER NO. 13, series of 1998
Duties (Safety Officer)
Direct accident prevention efforts in accordance with rules/ program
Conducts toolbox meetings everyday
Review inspections and accident investigation reports
Prepare and submit to DOLE minutes of committee meetings, work accidents and illnesses, and other reporting requirements
Assist government inspectors
Initiate/ supervise safety and health training for employees
Develop and maintain a disaster contingency plan

## Slide 22: Safety Inspection
Safety Inspection is a systematic way of identifying potential workplace hazards before they cause a health and safety problem.

## Slide 23: Safety Inspection
“An inspection is a service to an
organization
and its workforce; NOT a burden.”
Inspections are needed because nothing is completely risk-free...
Things wear out
Conditions change
People are not perfect

## Slide 24: Purposes of Safety Inspection
Eliminate Hazards
Assess Effectiveness of OSH Program
Display Visible Management
Commitment to Safety
Establish Accountability
Identify Training Needs
Fulfill Legal Obligations

## Slide 25: SALIENT FEATURES OF DEPARTMENT ORDER NO. 13, series of 1998
– Section 12: Safety and Health Information
A detailed safety and health information system is included in the guidelines. These include orientation, instructions, and training for workers; means of conveying safety related information to all workers and specialized instructions and trainings for specialty workers and operators

## Slide 26: SALIENT FEATURES OF DEPARTMENT ORDER NO. 13, series of 1998
General Safety and Health Measures
Basic rights and duties of workers
Emergency procedures
Good housekeeping
Welfare and first-aid facilities
Care and use of PPE
Personal hygiene and health protection
Safety and health rules and regulations
Daily tool box meetings

## Slide 27: Tool Box Meeting (TBM)
a 10-15 minute on-the-job safety and health awareness meeting focusing usually on the current activities of the group to keep everybody informed and alert on work-related accidents and illnesses and their causes.

## Slide 28: Benefits of a TBM
It addresses actual safety and health
concerns on the job or in the site
It provides good opportunity for supervisors to know the mental and physical conditions of workers
It also provides good opportunity for management to communicate its commitment to safety

## Slide 29: Benefits of a TBM
It contributes to the training and education of workers
It prevents the recurrence of previous accidents
It is a proven technique in
inculcating safe work habit

## Slide 30: Schedule
When:
Everyday before the start of work
Where:
Preferably at the specific site of the
activity
Who:
All workers in the site must attend their specific TBM

## Slide 31: Who conducts the TBM?
Usually the supervisor, foreman or leadman (the project manager, safety officer, nurse may serve as guests)

## Slide 32: SALIENT FEATURES OF DEPARTMENT ORDER NO. 13, series of 1998
Section 13: Construction Safety and Health Training
All safety personnel assigned within the construction site are required to undergo the basic construction safety training course prescribed by the Bureau of Working Conditions.
Continuing training (minimum of 16 hours per year) for all full-time safety personnel shall also be a responsibility of each constructor.

## Slide 33: Safety and Health Training
Basic Construction Safety and Health
Training (BOSH)
Continuing Training
(minimum of 16 hours per year)

## Slide 34: Specialized Instruction and Training
Operation of construction equipment
Erection or dismantling of scaffold
Excavation works
•
•
Workers engaged in pile-driving
Erection of steel structural frames and tall chimneys
Handling hazardous substances and
materials
Rigging and signaling

## Slide 35: SALIENT FEATURES OF DEPARTMENT ORDER NO. 13, series of 1998
Specialized instruction and training
Operation of construction equipment
Erection or dismantling of scaffolds
Excavation works
Handling of explosives
Workers engaged in pile-driving
Compressed air, cofferdams, and caissons
Erection of steel structural frames and tall chimneys
Handling hazardous substance and materials
Rigging and signaling

## Slide 36: SALIENT FEATURES OF DEPARTMENT ORDER NO. 13, series of 1998
Section 14: Construction Safety and Health Reports
The monthly submission of summary reports to DOLE is required. The summary reports shall include safety committee meeting agreements, accident investigation reports, and hazard assessments with corresponding remedial action/measures required.
Notification of major accidents to DOLE within 24 hours

## Slide 37: SALIENT FEATURES OF DEPARTMENT ORDER NO. 13, series of 1998
Section 15: Construction Worker’s Skills
A Skills certificate shall be required for construction related occupations which have been classified as “Critical Occupations” by TESDA.
An occupational shall be considered as critical –
  When it may affect and endanger people’s lives and limbs
  When it involves the handling of hazardous tools, equipment, supplies
  When it requires a relatively long period of education and training
  When the performance of the job may compromise the safety, health and environment concerns within the immediate vicinity of the construction site.

## Slide 38: Construction Workers Skills Certificate
TESDA shall:
establish national skills standards for critical construction occupations
prepare guidelines on skills testing and
certification
accredit construction sector organizations in
the area of skill training and trade testing
extend relevant assistance to construction sector organizations

## Slide 39: SALIENT FEATURES OF DEPARTMENT ORDER NO. 13, series of 1998
Section 16: Worker’s Welfare Facilities
The employer shall provide for adequate supply of safe drinking water, adequate sanitary and washing facilities in order to ensure humane conditions of work.
Section 17: Cost of Construction Safety and Health Program
The total cost of the Construction Safety and Health Program Shall be a mandatory integral part of the construction project. It shall be treated as a separate pay item and reflected in the project’s bid tender documents.

## Slide 40: SALIENT FEATURES OF DEPARTMENT ORDER NO. 13, series of 1998
– Section 19: Violations and Penalties
Violations committed by constructors as determined by DOLE after due process shall be considered as prima facie case of a construction mal-performance of grave consequence under RA 4566 (Constructors’ Licensing Law) as amended and pertinent IRR.
In cases of imminent danger situations, the procedures/requirements of the OSHS and DOLE regulations shall be applied.

## Slide 41: SALIENT FEATURES OF DEPARTMENT ORDER NO. 13, series of 1998
– Section 20: Effectivity
The Guidelines shall be immediately effective, that is, 15 days after publication in newspapers of general circulation, as provided in Article 5 of the Labor Code.
D.O. No. 13, s.1998 was signed on July 23, 1998 and published on August 1, 1998 in the Philippine Daily Inquirer and on August 3, 1998 in People’s Tonight

## Slide 42
RBA-ENVIRONMENT, HEALTH & SAFETY CONSULTANCY & TRAINING SOLUTION
Website: www.rba-ehscts.com
Email:rba.info@yahoo.com