## Slide 1
Personal Protective
Equipment

## Slide 2
Personal Protective
Equipment
Personal protective equipment are variety of devices and garments designed to serve as barriers between workers and workplace hazards.

## Slide 3: Head Hazards & Effects
HAZARDS
Impact from falling objects
Bump against rigid
stationary objects
Penetration by sharp objects
Contact with live electrical conductors
Fire hazards
EFFECTS
Perforation/fracture of the skull
Electrical shock
Burns

## Slide 4: Head Protection
Hard Hat or Safety Helmet
A rigid device that is worn to provide protection for the head and which is held in place by a suitable suspension.

## Slide 5: Parts of a Hard Hat
The suspension system includes the headband and straps on the inside of the hat. This system absorbs and distributes the force of impact.
The hard outer shell protects the head from sharp objects, such as falling tool. It also absorbs part of the force of impact, since it is somewhat flexible.
The chin strap secures the hard hat to the wearer’s head.
The brim redirects the direction of the falling object.

## Slide 6: Care and Maintenance
Wash with mild soap and water.

## Slide 7: Occupational Eye and Face Hazards
Large flying particles and fragments from operations such as chiseling, coarse grinding, hammering, metal working and riveting.
Dust, fumes, mists, and small particles from woodworking, light grinding, sanding, metal working, spot welding, scaling, and paint spraying.
Vapors and liquids from solvents and paints.
Intense heat and radiation from furnace tending, electric welding, and oxyacetylene welding and cutting.

## Slide 8: Effects of Occupational Eye and Face Hazards
EFFECTS
Permanent loss of vision
Temporary loss of vision
Inflamed eyes
Skin Burns
Lacerations
Fractures
Broken Teeth

## Slide 9: Eye and Face Protection
Protective eye and face equipment shall be required where there is a reasonable probability of injury that can be prevented by such equipment.

## Slide 10: Safety Spectacles or Glasses are primary protective devices intended to shield the wearer’s eyes from flying and striking objects, glare and injurious radiation hazards.
Sideshield is an integral device or an accessory attached to spectacles that provides side exposure protection to the eye.

## Slide 11: Goggles are primary protective devices intended to fit the face immediately surrounding the eyes.
Unlike safety glasses, goggles provide a secure shield around the entire eye area.

## Slide 12: Face Shield is a protective device intended to shield the wearer’s face, or portions thereof from striking objects or chemical, heat and glare hazards.

## Slide 13: When Should You Wear a Hearing Protection Device?
You should wear a hearing protection device whenever you are exposed to noise that is 90 decibels or greater for an 8-hour period of time.
A hearing protection device is anything that can be worn to reduce the level of sound entering the ear.

## Slide 14: ARM’S LENGTH RULE
“If two people (with no hearing impairment) have to raise their voices or shout to be heard in a distance of less than an arm’s length from each other, the sound level is potentially hazardous.”

## Slide 15: Types of Hearing Protectors
Earplugs
Hearing protectors placed inside the ear to block out noise. To work effectively, they should fit snugly into the ear canal.

## Slide 16: Types of Hearing Protectors
Earmuffs
A device composed of a headband with two cushioned ear cups that form a seal around the outer ear, covering it completely and blocking out the noise.

## Slide 17: RESPIRATORY HAZARDS
Acids/Mists
Solvents/Vapors
Gases / Smoke
Dusts/Particulates
Heavy Metals/Fumes

## Slide 18: RESPIRATORY PROTECTION
Filtration respirator
Chemical respirator
Air-supplying respirator

## Slide 19: FILTRATION RESPIRATORS or
Mechanical Respirators screen out dust and some form of mist. Such filters need to be replaced at frequent intervals.
CHEMICAL CARTRIDGE
DEVICES remove contaminants by passing the tainted air through material that traps the harmful portions. There are specific cartridges for specific contaminants.

## Slide 20: AIR-SUPPLYING RESPIRATORS
Self-Contained Breathing Apparatus (SCBA)
Supplies air from an air tank strapped at the person’s back or from a distant source.

## Slide 21: Hand and Arm Hazards
Temperature extremes
Chemical exposures and splashes
Sharp objects
Fire
Abrasive materials
Live Electrical Conductors

## Slide 22: Common Hand & Arm Injury
Burns
Bruises
Abrasions
Cuts
Punctures
Fractures
Amputations

## Slide 23: Different kinds of gloves
Metal mesh gloves resist sharp edges and prevent cuts
Leather gloves shield your hands from rough surfaces and heat
Vinyl & neoprene gloves protect your hands against toxic chemicals

## Slide 24: Different kinds of gloves
Rubber gloves protect you when working around electricity.
Welder’s gloves protect your hands from heat and flames
Cotton gloves help grasp slippery objects and protect against slivers, dirt, moderate heat or cold.

## Slide 25: Foot Hazards
 Falling or rolling objects
 Sharp objects
 Live Electrical conductors
 Hot surfaces
 Wet, slippery surfaces

## Slide 26: Common Foot and Leg Injury
Fractures
Punctures
Burns
Cuts
Amputations
Electrocution

## Slide 27: FOOT PROTECTION
Safety Shoes
Toe cap footwear protects your toes from being crushed by falling objects.
Mid-sole Device
protects the foot from punctured hazards.

## Slide 28: Safety Shoes and Boots
ELECTRICAL RESISTANCE
footwear are insulated with tough rubber to prevent shocks and burns from electricity.
ELECTROSTATIC DISSIPATING
footwear conducts static electricity to
floors that are grounded.

## Slide 29: Fall Restraint System
Travel Restriction System
- is an assembly composed of body belt and proper accessories that prevent a worker from traveling to an edge from where he or she may fall like leading edges or roof.

## Slide 30: Fall Arrest System
Fall arrest | system | are designed | to
minimize | stress | forces on | an
employee's body in the event of a fall, while providing sufficient freedom of movement to allow work to be performed.

## Slide 31: Components of a personal fall arrest system
Rope/Lanya rd

## Slide 32: Full-Body Harness
It consists of straps passed over the shoulders, across the chest, and around the legs. In a fall, a full body harness protects you more than a safety belt, because it distributes the force of impact over a greater area of your body.
L

## Slide 33: LIMITATIONS OF PPE
The hazard still exists.
A defective PPE offers no protection
The PPE may introduce additional hazard.
Most PPE are not for continuous use.
Improper wearing may not give maximum protection.
It may transfer hazard to another location.

## Slide 34: SUMMARY
For any PPE to be effective…
It must be selected based on use Employees must be trained on its use
It must be used and worn It must be maintained.

## Slide 35
RBA-ENVIRONMENT, HEALTH & SAFETY CONSULTANCY & TRAINING SOLUTION
Website: www.rba-ehscts.com
Email:rba.info@yahoo.com