## Slide 1
Demolition Safety
Notes: 1

## Slide 2
SAFE DEMOLITION REQUIRES ADEQUATE PLANNING
Why Plan?
Identify the Hazards
Meet Legislative Requirements
Ensure Appropriate Equipment
Ensure Safe Disposal of Materials
Determine Appropriate Methods of Demolition
Determine Cost of Demolition

## Slide 3
SAFE DEMOLITION REQUIRES ADEQUATE PLANNING
Key Areas for Planning
Type of Construction
Type of Structure (Use)
State of Structure
Structural Hazards
Hazardous Substances
Location of Services
General Conditions of Adjoining Structures
Access and Egress
Suitability of Site for Equipment

## Slide 4
DEMOLITION TECHNIQUE
Sequential – gradual reduction of height in reverse order to its construction
Induced – key structural members are weakened or removed, causing the whole part of the structure to collapse

## Slide 5
METHODS OF DEMOLITION
Manual – use of hand held tools
Mechanical – use of heavy equipment, wires and chain, power shear, etc.
Explosives – use of explosives

## Slide 6
Demolition Checklist Safety Tips
Has a demolition plan be though up? Has it been double checked to guarantee safety?
Have you Designated an area for the debris to be transported to after the demolition is complete?
Shut off all utilities before you start the job. These includes water, electric, sewer and gas. If any of these are left on, it could cause a major disaster.

## Slide 7
Demolition Checklist Safety Tips
Always begin at the top floor of the building and work your way down during a demolition.
If workers have to enter the building there should be braces placed on the floors and walls wherever there are people.
If you are using a floor disposal system the hole must be no larger than twenty five percent of the rooms floor.
Place chutes where ever you are disposing of debris from high areas. The chutes should lead directly to a trash container such as a dumpster.

## Slide 8
Demolition Checklist Safety Tips
Any ornamental stonework must be removed before the building is completely demolished.
All heavy machinery should be inspected by a certified professional before each job to insure it is in proper working condition.
Always wear your personal protective equipment while at a demolition site. This includes hard hats to prevent head injuries form falling debris. Safety goggles to prevent dust and other foreign objects form entering your eyes. Work boots that are made of leather and steel tipped will help protect your feet from falling objects.

## Slide 9
Demolition Checklist Safety Tips
Always inspect all personal safety gear before each use to make sure there are no cracks,dents or breaks that could compromise the equipment.
Are the people using the bulldozers and cranes trained in the safe way to operate the heavy machinery?

## Slide 15
RULE 1417 - 1418: DEMOLITION
1. Structures over 6m high must be under the supervision of a competent person
2. The area is strictly for demolition workers only (Demolition area - w/in a distance equal to 1.5 x H of structure)
3. If the above distance is not possible, the structure shall be fenced around
4. Danger signs should be posted around the structure
5. Ensure all electrical services are cut-off

## Slide 16
OSHS RULE 1417 - 1418: DEMOLITION
7. Demolition should proceed storey by storey, in a descending order; work on the upper floors should be completely over before removing the supporting members on the lower floor
8. No part of the structure shall be overloaded w/ debris or materials.
9. Stairs (incl. railings), passageways & ladders should be demolished last

## Slide 17
HAZARDS ASSOCIATED WITH DEMOLITION
Falls
Being Hit/Trapped/Crushed by Objects
Manual Handling
Hazardous Substances and Dangerous Goods
Noise and Vibration
Electric Shock
Fires and Explosions
Equipment

## Slide 18
EXPLOSIVES
By Competent Person
Precautions from:
Smokes, matches & open flames
Radio Frequency for Electrical Detonators
Transport of Explosives
  Vehicles shall have tight floors covered w/ wood
  Explosives and Blasting implements shall not be transported with other materials

## Slide 19
EXPLOSIVES
Storage
  All explosives must be accounted for
  Follow manufacturer’s instructions
  Detonators should be stored in a separate magazine
  Storage should be fire and bullet-resistant
Proper Use
  Operation between Sunup & Sundown
  Precaution on the use of f mobile radio transmitting equipment.
  Suspension of operation during electrical storm

## Slide 20
EXPLOSIVES
After Blasting
  Disconnect firing line from blasting machine
  Allow dust and smoke to subside
  Inspect if all charges have been exploded

## Slide 21
RBA-ENVIRONMENT, HEALTH & SAFETY CONSULTANCY & TRAINING SOLUTION
Website: www.rba-ehscts.com
Email:rba.info@yahoo.com