## Slide 2: OBJECTIVES
At the end of this session, the participants will be able to:
Describe the chemistry, behavior and concept of fire.
Understand the principles of fire prevention, suppression and control.
Recognize the important elements of an effective Fire Safety Program
Recognize the causes and extent of fire incidents
Notes: Objectives: “Recognize the important elements of an effective Fire Safety Program – of course, 1st thing important is you learn because you are SO’s. But it shouldn’t end there, you have to translate the learning to actual programs in your workplace. Implement Fire Safety Programs. Joke: wag naman update lang ng resume.
“Recognize the causes and extent of fire incidents” – To know the importance and significance of this subject matter.
“Describe the concepts and understand principle of fire…” – We have to understand the nature, concept and principle first in order to understand fully the objectives of this subject matter.
·Categories of Fire
  Beneficial (controlled) – e.g. for cooking, internal combustion engines, heating and lighting, etc.
  Destructive (uncontrolled)
·We are suppressing “destructive fires”, those that may result to injury, illness, death and damage to property.
Analogy of soldier using a gun and a person using a gun. That is, you need to understand the behavior of your enemy. You do not survive in a war with a knowledge only on how to use the gun. You have to know the behavior of your enemey. That’s how we should face fire.

## Slide 3: TOP CAUSES OF FIRE IN THE PHILIPPINES
Electrical
  a. Defective/Faulty Wiring
  b. Overloaded Circuits
  c. Inoperable Safety Devices
  d. Overheating
Open flames and candles
Liquefied Petroleum Gas (LPG)
Smoking and Matches
Friction
Combustion Sparks
Static Electricity
Lightning
Spontaneous Ignition
Nature
*BFP Data
Notes: Flashover – Everything will burn spontaneously due to intense heat (due to radiant heat). A flashover is the near simultaneous ignition of all combustible material in an enclosed area. Flashover occurs when the majority of surfaces in a space are heated to the point (known as fire point) at which they give off flammable gases that are hot enough to sustain combustion. Flashover normally occurs at 500 °C (930 °F) for ordinary household combustibles. – (reference wikipedia)
Spontaneous ignition: oily rags left under direct sunlight will burn under atmospheric condition without the introduction of source of ignition.
Auto ignition/spontaneous combustion – example: Potassium Chlorate – sensitive to heat.
Instantaneous combustion (soiled rags, i.e with oil then heated by the sun then ignite combustible materials)
LPG Facts
  LPG is not toxic or poisonous but displaces the air.
  “Ethyl Mercaptan” is mixed with “odorless” LPG to have a warning sign in case of leak. Odor is added for detection of leaks
  60 % Butane and 40 % propane
  Store upright as liquid may damage the valves (nakababad).
  Can be leak tested using soap solution
  Heavier than air, will go to ground depression or will displace air inside a room
  Never open or turn of electrical appliances/switches
  Open windows in case of leaks
  Do not explode by itself. Just simply close the regulator if the stove/hose catch fire. What explodes is the room when saturated by LPG then you turn on and off the light in an enclosed room…. Just simply open the doors and window. Story of someone threw the lpg tank thinking that it will explode

## Slide 4: TRAGIC FIRE INCIDENTS IN THE PHILIPPINES
OZONE DISCO FIRE : 162 DEATHS plus INJURIES
LUNG CENTER FIRE: 25 DEATHS plus INJURIES
DAMAS de ISLAS de FILIPINAS FIRE: 23 DEATHS plus INJURIES
QC MANOR HOTEL FIRE: 75 DEATHS plus INJURIES

## Slide 5: CAUSES OF FIRE DEATHS
1. Inhalation of Toxic fumes:
– Carbon Monoxide (CO)
– Carbon Dioxide (CO2)
– Hydrogen Cyanide (HCn)
– Nitrous Oxide (N2O) / Nitrogen
– Dioxide (NO2)
– Fluorides (F) and Chlorides (Cl)
Notes: Burning plastic releases dioxin which causes cancer

## Slide 6: CAUSES OF FIRE DEATHS
2. Insufficient oxygen (Asphyxia)
3. Effects of heat (Hyperthermia)
4. Bronchial and pulmonary swelling (Edema) with blood congestion (Hyperemia)
5. Ventricular fibrillation
6. Backdraft or smoke explosion
Notes: Backdraft – air drawn in room under fire. A backdraft is a situation which can occur when a fire is starved of oxygen; consequently combustion ceases but the fuel gases and smoke remain at high temperature. If oxygen is re-introduced to the fire, eg. by opening a door to a closed room, combustion can restart often resulting in an explosive effect as the gases heat and expand. – (reference wikipedia)
Ventricular fibrillation – Condition in which the heart’s electrical activity (electrical signals) become disordered. Heart pumps little or no blood.
Carbon Monoxide – odorless and colorless

## Slide 7: FIRE SAFETY
FIRE PREVENTION – Preventing occurrence of destructive fire or reduce likelihood of destructive fire.
FIRE SUPPRESION – Extinguishing unwanted/ uncontrolled destructive fire. Means of mitigation. Reduce the effect of destructive fire.
FIRE EMERGENCY PREPAREDNESS – Preparing persons in the eventuality of a fire emergency.
Notes: Fire Prevention: Prevention of 5 P’s (People, Property, Product, Process and Profit).

## Slide 8: FIRE PREVENTION PRACTICES
Correct all defective wiring systems.
Never overload a power outlet.
Unplug all appliances that are not in use.
Never bypass fuses or circuit breakers.
Never play with matches or lighters
Always keep stoves that use LPG’s in good condition
Practice safe storage of chemicals
Smoke only in designated smoking areas.
Notes: ·Story of an auto-electrician approximating the number of strands of an electrical wire as substitute to a standard fuse… and that ultimately resulted to damaged part of the vehicle.
·Fire prevention practices
  o Correct all defective wiring systems. Spliced wires must be repaired or replaced and substandard materials should not be used. Wire terminals should be done correctly.
  o Never overload a power outlet. Do not connect too many electrical appliances to one outlet. Use extension cords only for low power equipment.
  o Unplug all appliances that are not in use. Never leave energized appliances which produce heat such as iron, electric stoves, electric fans, hair blowers, etc.
  o Never bypass fuses or circuit breakers. Replace blown fuses and defective breakers with standard items and with the same rating.
  o Never play with matches or lighters. Candles must be placed on areas away from curtains and other combustible and flammable materials. Keep matches, lighters and candles away from children.
  o Always keep stoves that use LPG’s in good condition. Replace old, cracked gas hoses with new ones as soon as possible. If you smell a leaking LPG, never turn “ON” or “OFF” lights and other electrical appliances. Open all windows. Discard corroded and rusted LPG Tanks.
  o Practice safe storage of chemicals by keeping flammable and combustible materials away from flames, any source of heat and direct sunlight.
  o Smoke only in designated smoking areas. Strictly obey “No Smoking” signs. Throw cigarette butts only in cigarette bins or ashtrays.

## Slide 9: PRINCIPLES OF FIRE PREVENTION AND CONTROL
• Prevent the Outbreak of Fire
• Provide for Early Detection
• Prevent the Spread of Fire
• Provide for Prompt Extinguishment
• Provide for Prompt and Orderly Evacuation
Notes:   Prevent the outbreak of fire – keep 3 elements separated
  Provide the early detection of fire – because it’s easier to manage fire in it’s early stages. Install signal/alarm systems.
  Prevent the spread of fire – confine it to the smaller area possible. Install fire walls, fire doors, dampers, dikes, etc.
  Provide for prompt extinguishment of fire – fire suppression equipment (fixed and permanent). Fire hose should be drain and tested every 4 months.
  Provide for the immediate evacuation of personnel – drills, evac maps,2 exits/floor, emergency preparedness and response plans

## Slide 10: WHAT IS FIRE?
It is frequently referred to as “rapid oxidation with the evolution of light and heat.”
Fire is a chemical reaction between a flammable or combustible material and oxygen.
Is the chemical union of heat , fuel and oxygen produced in the proper proportions
Notes: Comparison of rust (slow oxidation). Coal (fossil fuel from forests-middle east) with rapid oxidation. Atmospheric (or slow) oxidation = resulted to rust of metals. Rapid oxidation = resulted to burning of oxygen which resulted to “rusted” like appearance. The heat made oxidation rapid. Things are exposed to oxygen and thus undergoes oxidation. The head made oxidation rapid. Oxidation means introduction of oxygen.

## Slide 11: TRIANGLE OF FIRE
Any material that will burn is classified as fuel
FUEL
Reducing Agent
Notes: Wag na nating pagtularan kung fire triangle, fire tetrahedron or fire pyramid. Those are just terms of various fire training organizations.
Observe a burning wood – it seems that the fire is floating, because what burns is the vapor of the wood and not the solid wood. Heat vaporizes the wood.
“solids ay di nasusunog” (vaporize first). That’s why you can’t see the fire “touching” the solid fuel when you look closely. Yung vapor ng utem ang nasusunog. Heat will vaporize the solid first.

## Slide 12: FUEL
Flash point - is the lowest temperature at w/c fuel gives off flammable vapors.
Flammable material – a material having a flashpoint below 100F (37.8C).
Flammable Substances Flashpoint F C Gasoline -45 -42.8 Ether -49 -45 Acetone 0 -17.8 Alcohol 55 12.8
Notes: Nasusunog lang ay organic, with the exception of heavy metals
Ignition temp: the temperature of a substance in order for it to have a continuous, self sustaining fire.
Flammable and inflammable are the same.
Combustible and incombustible are not the same
Fire Point - the temperature at which a fuel will continue to burn after it has been ignited. This is a few degrees hotter than the flash point
Flash Point - the lowest temperature at which a substance will give off enough vapors to form a flammable mixture with air near the surface of the substance that will burn when a flame or spark is applied

## Slide 13: FUEL
Combustible material – a material having a flashpoint at or above 100F (37.8C).
Combustible Substances Flashpoint F C Fuel Oil 100 37.8 Kerosene 100 37.8 Quenching Oil 365 185.0 Mineral Oil 380 193.3
Notes: When storing chemicals – take note of the vapor pressure. The higher the vapor pressure of the material the more vulnerable the container. The weakest portion of the container will be the first to give-in. An open container which contains a volatile material actually releases freely due to evaporation (release of the vapor pressure)

## Slide 14: WHICH IS MORE DANGEROUS
Question: A substance with low flashpoint or a substance with a high flashpoint?
Answer: The lower the flashpoint, the more dangerous a substance is.
Question: How would you know the flashpoint of a substance?
Answer: By looking at the label or even MSDS. Or even by searching in the internet.
Notes: Flammable is more hazardous because it can easily be ignited, however, combustible materials on fire are much more difficult to suppress.

## Slide 15: OXYGEN
Normally, air is 21% oxygen and 78% nitrogen.
OXYGEN
Oxidizing Agent

## Slide 16: OXYGEN
When oxygen content of air drops below 16%, the fire will normally go out for lack of oxygen.
In an atmosphere of pure oxygen, many substances not normally considered combustible will burn rapidly. Atmosphere of pure oxygen or even oxygen enriched air will produce fire of great intensity.
Notes: Oxygen Level
  Max Safe Level = 23.5 % (OSHA)
  Normal Level = 21 % (78% Nitrogen, 1 % Other Gases)
  Minimum Safe Level – 19.5 % (OSHA)
  16 % - Minimum level to support fire
  Most people die from lack of oxygen than fire
  Above 23 % – considered as oxygen enriched

## Slide 17: HEAT
Flames, cigarettes, matches, hot surfaces,
lasers, thermal sparks, welding torches, friction, etc
HEAT
Notes: Static electricity: rubbing of wool. Fire incidence in a gas station. A lady was rubbing her hands on her clothes while handling the gas pump and nozzle. The gas vapors suddenly goes into flame

## Slide 18: SOURCES OF HEAT
Electrical Heat Energy
Arcing
Welding and Cutting Sparks
Mechanical Heat (friction heat)
  Slipping belt against pulley
Friction Spark
  Dropping steel tools on a concrete floor
Open Flames
  Cigarettes, matches, welding torch, internal combustion engines
Notes: Relative Humidity: amount of moisture in the air.
  Arizona: RH = 12 – very dry/little moisture content –
  Note: RH below 20 is prone to static electricity which is a Fire Hazards.
  Philippines RH = 90. Too humid (malagkit). Prone to dusty air. Prone to “libag”
  Safe and Ideal RH = 40 to 60

## Slide 19: ELEMENTS OF FIRE (FIRE TRIANGLE)
FROM AIR
HEAT SOURCE
GASES
LIQUIDS
SOLIDS
FUEL
Reducing Agent
HEAT
OXYGEN
Oxidizing Agent
Chemical
Reaction
Notes: Flame Color
  Blue – good or complete combustion. complete combustion, highest temp, CO2 is by product
  Yellow – poor or incomplete combustion. incomplete combustion, low heat, produces CO
  White Flame – metal flame (don’t pour water, it may explode)
Smoke color
  Gray smoke – with fumes and other buproducts
  White smoke: grassfire
·Joke/story-Fire triangle: man, wife and mistress

## Slide 20: CLASSES OF FIRE
Class A - Ordinary Combustibles E.g. wood, paper, rubber, plastic etc
Class B - Surface Fire (flammable/combustible liquids and gases)
E.g. gasoline, alcohol, paints, thinner, grease, LPG release of gas
A
B
Notes: Ordinary combustibles – with residue or ember
Surface fire – without residue.
If an electrical equipment is not energized (under fire), it’s classified as Class A or B.

## Slide 21: CLASSES OF FIRE
Class C - Electrical Fire (Involves live electrical equipment)
E.g. motors, electric fan, air-conditioning unit, computer etc
Class D - Combustible Metals
E.g. magnesium, sodium, titatium, etc.
Class K – Kitchen Fires
Recently recognized by NFPA 10.
Fires involving combustible vegetable or animal non-saturated cooking fats in commercial cooking equipment.
C
D
Notes: Type K Fires (cooking oil) – use “K” type fire extinguisher or potassium carbonate type
·Type E- fire = Combination of any two types

## Slide 22: HEAT TRANSFER (HOW FIRE IS SPREAD)
Conduction – transfer of heat from molecule to molecule
Convection – caused by movement of heat gasses produced by any burning material
Radiation – transfer of heat rays in straight rays
Notes: Joke/story : Analogy of bonfire and mode of spreading fire (barbecue-conduction, tree/leaves-convection, warmth-radiation). “with the sweetheart”
Conduction – can be direct contact with the fire or through a conductive material.

## Slide 23: EXTINGUISHMENTS OF FIRE
Removal of Fuel
Excluding or Limiting Oxygen
Cooling
By Interrupting the Chain Reaction
Notes: Removal of fuel: Starvation, ex gasoline station pumps and underground storage tanks. LPG and stove. Suppression actually depends on the practicality of the approach. Would you consider removing the tables or other combustibles in the room whenever there is a fire?(starvation approach)
Excluding or limiting oxygen: blanketing. Dry Chem Portable Fire Extinguisher uses blanketing principle.
Grass/bush fire – sinusunog intentionally using blow torches at pag cut sa mga pinong kahoy para magkaron ng putol sa pag spread. (“fire break”)

## Slide 24: PERMANENT FIRE EXTINGUISHERS
Standpipe and Hose
Automatic Sprinkler System
Fire Hydrant
Fire Pump
Fire Truck
Automatic fixed fire extinguishing system (Ex. FM-200)
Notes: FM-200 – decrease oxygen concentration inside the room

## Slide 25: PORTABLE FIRE EXTINGUISHERS
DRY CHEMICAL
CARBON DIOXIDE
AFFF
WATER
HCFC-123
DRY POWDER
D
Notes: ·Joke/story – using PFEX is like like granada (pero di iniitsa ha)
Portable Fire Extinguisher
  90-92% Mono-Ammonium-Phosphate is good.
  DTI and BFP certification is not mandatory
  Locally produced – BPS (Bureau of Product Standards) mark of DTI
  oBPS is the sole agency which issue and approve licenses to assemble PFEX
  BPS (Bureau of Product Standards) is the sole agency which issue and approves licenses to assemble PFEX (i.e. “PS Quality Mark”
  NFPA 10 – NFPA standard for PFEX
  In the US, PFEX must comply with ANSI/UL standards (imported units)
  “It is illegal and unethical for firemen to act directly or indiscreetly as salesmen of PFEX.
  First 3-4 minutes of fire is critical if you will be able to suppress it or not.
  FAQ: Is it harmful on the user? Ans: Excess is always harmful but you will only use it at most probably once in your life. And it’s better to use it than let the fire consumes everything. In fact, I have come across with a supplier who even tastes the chemical to show that it is not toxic. But do not try it at home or at your office.
  Do not us as door stopper or “pang-kalso”
  1944.05 Requirements: Top should be not mor ethan 1.5 above the floor and should be in brackets or hangers. For 18 kg unwheeled type, top should not be 1 m off the floor.
  For class A fires: Travel not more than 30 m and 1 unit/250 sq. m. Add units on more hazardous areas.
  FAQ: 1 year replacement and/or recharge?
    1944.05 (g)”at regular intervals of not more than one year, or when specifically indicated by an inspection, extinguishers shall be thoroughly examined, recharged or repaired.
    Why: It is assumed that agent can “cake” in one year’s time due to moisture entering the cylinder. Dry Chem actually does not expire but we are just making sure that air has not been able to seep through the fittings.
  Should be hydrostatically tested every 5 years.
  Multipurpose dry chem should be at the green zone (gage). Slightly greater than green is no problem as long as it doesn’t exceed the midway point between the green zone and the max limit
  Halotron agent: Dichloro Triflouroethane - HydroChloroFluoroCarbon (HCFC). Specifically used for electronic equipment such as computers, UPS, servers, etc. – non-corrosive agent.
    Non-expirable
    Non-Corrosive to metal, electric and electronic parts
    No residue/ non-conductor
    Most effective when used in an enclosed space (indoor)
    Multi-shot

## Slide 26: PARTS OF A PORTABLE FIRE EXTINGUISHER
TRIGGER
HOSE
NOZZLE
(DISCHARGE OUTLET)
TANK/
CYLINDER
LABEL/INSTRUCTIONS
PIN
GAUGE
MOUNTING/ BRACKET
TANK BASE
GAUGE
PIN
SEAL
DRY CHEM TYPE PORTABLE FIRE EXTINGUISHER
Notes: Sodium bicarbonate – baking soda
PFEX should be recharged after every use even though the pressure is still ok or even though it is just partially or slightly used.

## Slide 27: INSIDE A PORTABLE FIRE EXTINGUISHER
STORED PRESSURE
DRY-CHEM TYPE PORTABLE FIRE EXTINGUISHER

## Slide 28: FIRE EXTINGUISHER REQUIREMENTS
Approved Type
The Right Type for the Class of Fire
Sufficient Quantity
Accessibly Located
Maintained in Operating Condition
Operable by Trained Personnel

## Slide 29: USING FIRE EXTINGUISHER
P = Pull the Pin
A =
Aim the Nozzle
S = Squeeze the trigger
S = Sweep side to side
at the base
Notes: Dapat alam na ang pag-gamit ng PFEX, hindi yung pag may sunog na saka lang babasahin ang instruction. Baka too late or past incipient stage nay un. Yun ang important kaya kailangang may training on this. Using PFEX is very easy but in emergency situation, people tend to panic. Kaya dapat alam na beforehand ang tamang pag-gamit

## Slide 30: USING FIRE EXTINGUISHER
Start approximately 6-8 feet from the fire then squeeze the trigger slowly while moving towards the fire
10-lb fire extinguishers lasts only 10-20 seconds. It should be used correctly.
When the fire is extinguish, stop pulling the trigger. In the event of a re-ignition, at least there would still be contents inside the unit.
Ensure that you have an escape path in case the fire is not extinguished

## Slide 31: FIRE DETECTION AND ALARM SYSTEM
complete protective signaling and control system i.e. fire detection, alarm and communication primarily intended to provide the indication and warning of abnormal conditions,
summoning of appropriate aid
Notes: Annunciator – connected to the FDAS system which indicates where the alarm (automatic-detector or manual pull station) originated. It consists of an area map with LED lights indicating the location of the alarms.

## Slide 32: TYPES OF DETECTORS
Smoke detectors
Flame detectors
Thermal/heat detectors
Notes: Smoke detectors – should have a blinking LED that indicates that it’s active and working

## Slide 33: EXTIGUISHMENT OF FIRE
REMOVAL OF FUEL (STARVATION)
LIMITING OXYGEN (SMOTHERING)
REMOVAL OF HEAT (COOLING OR QUENCHING)

## Slide 34: EXIT SAFETY
Travel Distance
Clear, Unobstructed & Lighted
Regular Exit Drills
At least 2 ways out
Correct Exit Design
Notes: ·When your clothing catches fire – “Stop, Drop and Roll”. Do not run.
·Evacuation- It is very important to shut the door (but do not lock it) during evacuation to prevent spreading of fire.
·3 components of means of egress
  o Exit (exit point)
  o Exit Access
  o Discharge (assembly point)
·When someone get injured, don’t move him, unless he is in dire situation (i..e, he will get burned). Baka sisihin nyo ko pag nangyari yun, “uy yung lecturer namin sinabi wag daw gagalawin….” Until masunog na.

## Slide 35: HOT WORK PERMIT
An administrative control of controlling fire hazards (fire prevention).

## Slide 36: HOTWORKS
Welding and Cutting Sparks
Notes: Rule 29 SEC 39.106 of the Fire Code and Rule 1100 of the Occupational Safety and Health Standards state that welding and cutting operations shall not be done in or near rooms or locations where flammable liquids or vapors, or combustible materials are located.
As for the minimum distance, you may refer to the US Occupational Safety and Health Administration (OSHA) and the US National Fire Protection Association (NFPA) standards particularly OSHA Standard # 1910.252 and NFPA 51B in wherein the recommended clearance between a hot work area (e.g. welding, cutting and brazing operations) and combustible and flammable materials is at least 35 feet (10.7 meters).

## Slide 37: ORGANIZING THE FIRE BRIGADE
FIRE BRIGADE – a group of employees organized & trained to respond to fire emergency in the plant before professional help arrives.
The SIZE OF THE FIRE BRIGADE depends on:
  Size and area of the plant
  Manufacturing process
  Materials handled
  Plant location in relation to outside help

## Slide 38: QUALIFICATION of FIRE BRIGADES
FIRE BRIGADE CHIEF
  Sincerity
  Capacity to do the job
  Leadership
FIRE BRIGADE MEMBERS
  Able-bodied
  Willing to do the extra work
  Capacity and desire to be trained
  Available for fire duty

## Slide 39: DUTIES OF THE FIRE BRIGADES
Fire Prevention
  Conduct fire safety inspections.
  Repair and maintain fire fighting equipment.
Fire Control & Extinguishment
  Fire alarm/call from the fire department.
  Direct the evacuation of personnel, important documents, equipment, etc.
  Shut off power/machinery, gas, etc.
  Extinguish fires.
  Move motor vehicles away from plant.
  Conduct salvage operations.
  Take steps to prevent recurrence.

## Slide 40: FIRE FIGHTING TEAM
FIRE BRIGADE CHIEF
Assistant FIRE BRIGADE CHIEF
FIRE
EXTINGUISHER
HANDLERS
FIRE
HOSE
HANDLERS
NOZZLE
HANDLERS
Stationary
FIRE PUMP
OPERATOR
WATER
SPRAY
OPERATOR
WATER
SPRINKLER
SYSTEM
FIRE
SUPPRESSION
SYSTEM
WATER
SUPPLY
Portable
FIRE PUMP
OPERATOR
FIRE
TRUCK
SAFETY
OFFICER
Automatic
FIRE ALARM
SYSTEM
Other FIRE
EQUIPMENT,
Ladder, SCBA, Etc.

## Slide 41: EMERGENCY CONTROL ORGANIZATION
Emergency Control Commander
Chief Executive Officer
DISASTER CONTROL
Assistant CEO
FIRE
FIGHTING
TEAM
UTILITIES
CONTROL
TEAM
SALVAGE
TEAM
COMMUNICATION
TEAM
SEARCH &
RESCUE
TEAM
SECURITY
TEAM
TRANSPORT
TEAM
FINANCE &
INSURANCE
TEAM
WATER
FUEL Oil & LPG
ELECTRICITY
GENERATORS
Compressed Air
WW Treatment
  Facility
PAYLOADER
TRUCKS
FORKLIFT
Etc.
DOCTOR
NURSES
FIRST AIDERS
SEARCHERS
MONITORS
EXIT GUIDES
FIRST AID
  Station
Plant Gates
Plant Traffic
Evacuation
  sites
Fire Trucks
Visitor
  Control
Service
  Vehicles
Pick-Up
  Points
Ambulance
See FB
Organization
SAFETY
OFFICER
ENVIRONMENTAL
OFFICER
INTERNAL
EXTERNAL

## Slide 43: FIRE SAFETY PROGRAM An effective Fire Safety Program must have the following:
Fire Detection and Alarm System
  Fire Alarms, Detectors, annunciators
First Aid Fire Protection System
  Portable Fire Extinguisher
Fixed Fire Protection System
  Sprinklers, Hydrants, Fire Hose/ Fire Hose Cabinets
Fire Exit Doors, Fire Exit Signs, directional arrows
Fire emergency evacuation route maps/evacuation plans
Inspection and maintenance system of fire detection, alarm, control and suppression systems.
Hot work permit system
Fire Safety Training
  Fire Principle
  Use of Portable fire Extinguishers and other fire fighting equipment.
Conduct of drills
Working/active fire brigade team/ emergency response team
Working/updated Emergency Response Plans
  Response Procedures (What to do’s)
  Emergency contact numbers
  Contingency and communication plan
  Assembly area/assembly plan.
Compliance to standards (OSHS, Fire Code)
Notes: Sad but true: compliance lang ang usual reason ng management kaya lahat ng attendees would say “ako ang ina-sign eh” or “napilitan kasi wala ng iba”… hindi because of malasakit or desire na walang masasaktan sa mga employees… that’s the reason kaya hindi sustainable ang safety and health program kasi nga compliance lang ang habol.
This training is very important to you because you are safety officers, however don’t just treat this training as a “personal gain” training or “nice to know training”, you should apply all the learnings in your respective companies. Translate your learnings into programs. That is the main reason why you attended this seminar. After undergoung the training, the next thing is to apply and echo this training to your companies and not just updating your resumes

## Slide 44
RBA-ENVIRONMENT, HEALTH & SAFETY CONSULTANCY & TRAINING SOLUTION
Website: www.rba-ehscts.com
Email:rba.info@yahoo.com